## Slide 1
Status of the ESRF-EBS 352 MHz RF system
Jörn Jacob, Pawel Borowiec, Vincent Serrière, Alessandro D’Elia
26th ESLS RF Meeting – Elettra
Trieste, 8-9 November 2023

## Slide 2: outline
ESRF upgrade: EBS
352.37 MHz RF system for EBS
  RF layout
  HOM damped ESRF cavities
  RF ECO-Mode
  RF trips 2023 (so far)
RF projects
  Replacement of klystrons by 10 SSAs
  4th harmonic RF system

## Slide 3: ESRF EBS upgrade
200 MeV Linac
6 GeV Booster
6 GeV Storage Ring
200 mA
ESRF = First 3rd generation Storage Ring Light Source
1992: commissioning
1994: external users
since then:
many upgrades
brilliance increase by about a factor 1000
Up to 100 keV X-rays
2020 New Extremely Brilliant Source: EBS
First 4th generation high energy light source
further brilliance increase by a factor 40
Substantial gain in coherence
Circ = 844 m

## Slide 4: EBS 352.37 MHz RF system Layout
EBS Storage Ring
NEW Teststand: in new adjacent building
KLYS 2
Cell 7
KLYS 1
Cell 5
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
3x existing 150 kW SSAs
Cell 25
-7 dB
-7 dB
Space for 4th harmonic RF system
Symmetric 3dB splitting using existing magic T’s
1.1 MW Thales klystron

## Slide 5: MAIN RF parameters for ESRF-EBS upgrade
Total energy loss: 3.2 MeV/turn
    Energy loss from dipole radiation: 2.5 MeV/turn
    Energy loss from ID radiation, up to: 0.7 MeV/turn
Nominal RF Voltage: 6.0 MV
13 HOM damped cavities: 0.5 MV to 0.75 MV/unit
Nominal stored current: 200 mA
EBS 30 % less total RF power than old machine:  1 MW at nominal 200 mA

## Slide 6: HOM damped single cell cavities 13 units on the storage ring
fres | 352.372 | MHz
Q0 | 35700 | (measured)
R/Q | 145 | 
Rs |  5 | M
Tuning range | -350 / +900 | kHz
Vacc nominal / max | 500 / 750 | kV
Coupling  | 2.8 | 
[ESRF design by Vincent Serrière]

## Slide 7: RF system – power levels
To give an idea:
Cavity dissipation: Pc = Vacc2 / (Ncav x 2Rs) = 300 … 400 kW (including reflected power)
Beam power: Pbeam = Ibeam x Utot/e, = 500 … 700 kW at 200 mA
(Utot = U0 + UID , U0 = 2.5 MeV/turn, UID = 0…1 MeV/turn)
Total RF power: = 800 … 1000 kW at 200 mA
AC to RF conversion efficiency: = 30% … 52 %
AC power  f(Ibeam, UID): = 900 kW … 1900 kW

## Slide 8: Explosion of Energy cost Autumn 2022  RF ECO Mode
PAC = [ Vacc2 / (Ncav x 2Rs) + Pbeam ] / RF/AC
ECO mode:
Reduction of total Vacc from 6.0 to 5.5 MV
Increase AC to RF conversion efficiency:
  10 years old 150 kW SSA in cell 25 haven’t yet drain voltage modulation and are operated way below nominal power (90 …100 kW), where the efficiency is low. NB: new SSA from JEMA will have drain voltage modulation and better efficiency at low power like klystrons with anode modulation !
  Increase the share of Klystron power by increasing Cav 1 to 10 voltage from 4.5 to 5.0 MV
  Operate with only 1 SSA e.g. Cav 13 at 0.5 MV
  Gain in efficiency over-compensates adverse effect of lower Ncav
RESULT:
200 kW AC power savings at 200 mA
Same beam lifetime for typical ID losses around 0.4 … 0.5 MeV/turn

## Slide 9: Operational statistic as of 31/10/2023
Chart: Events by equipment
| Cavities | Tra1 + auxiliaries
Events by equipment | 10 | 7
Chart: Tra1 by type of event
| EEV-4 klystron | HVPS | Auxiliaries
Tra1 by type of event | 3 | 1 | 2
EEV-4 klystron:
Ion pump #1 – action: disconnected from operation
Breakdown in the input cavity
HVPS:
Internal control issue – loss of the output voltage, no diagnostic available thus external data logger installed in the thyristor room to monitor parameters
Auxiliaries:
Magic Tee0 load flowmeter broken – exchanged
hiccup with the regulation loops of TRA1 -> procedure updated

## Slide 10: Cavities in 2023
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
Cavity distribution | 0 | 0 | 0 | 0 | 0 | 1 | 3 | 1 | 2 | 2 | 0 | 0 | 1
Chart: Type of Event
Chart: Filling Mode
Chart: Cavities by type of event
| Breakdown | Pressure Burst
Cavities by type of event | 8 | 2
Chart: 
| Run 1 | Run 2 | Run 3 | Run 4
Distribution by run | 2 | 2 | 3 | 3
Chart: 
| 7/8 +1 | 16 BUNCH | UNIFORM
Filling mode | 7 | 2 | 1
Cell 7
No signs of degradation nor significant deviations of cavity parameters w.r.t. cavities in other cells have been observed.

## Slide 11: Gradual implementation of 10 SSA (each 110 kW RF, max 250 kW AC)
Cell 7
KLYS 1
Cell 5
3 existing 150 kW SSAs / ELTA
KLYS 2
Space for 4th harmonic RF system
2024
2024
2024
2024
2025
2026
2026
Dec.
Keep Klystron 2 as a unique high power RF source for the teststand
01
02
03
04
05
06
07
08
09
10
13
12
11
2026
2026
Dec.
2025
Cell 25
Klystron 1 dismounted in Autumn 2026 to free space for last 2 SSAs for cavities 04 and 05
SAT for each SSA connected to RF power teststand, switching between:
cavity in teststand and
load with variable mismatch (EH tuner)
 RF Teststand
10 new 110 kW 352 MHz SSAs
by JEMA France
Site preparation in good progress:
All within existing buildings
New transformers and power switchgear rooms under existing roof
20 kV and 400 V cables pulled
Installation of pre-fabricated water cooling manifolds and piping in progress
Waveguide layout designed, building adaptation done
LLRF and Control system in progress

## Slide 12: 4th harmonic RF system for bunch lengthening
For all modes: Hor. Emit. z = 135 pm | Multibunch 7/8 filling | 16-bunches | 4-bunches
Total current | 200 mA | 92 mA | 40 mA
Current per bunch | 0.23 mA | 5.75 mA | 10 mA
Bunch length (calc.) | 13 ps | 31 ps | 37 ps
Vert. Emit. z set at | 10 pm | 20 pm | 40 pm
Touscheck Lifetime | 33 h |  4,5 h |  4 h
    1st Priority for high I / bunch (16 bunch and 4 x 10 mA)
    Reduced Touschek scattering, IBS and microwave instability:
      Factor 2.5 to 3 increase in Touschek lifetime  less frequent injections, reduced loss rate and radiation load
      Improved overall stability
      Reduced emittance and energy blow up
      Room for smaller In-Vacuum ID gaps
      Maybe 20 pm  10 pm vertical emittance in 16b and 4b
      Alleviate possible impact from future lattice developments like mini-beta straights
    Reduced heat-load and stress of critical chambers, like ceramic chambers or In-Vacuum IDs
H4 @ 1.41 GHz
Bunch lengthening by a factor 2.5 to 3
Latest harmonic cavity design

## Slide 13: 4 single cell TM020 cavities, f =1409.45 MHz - Latest design evolutions
3 Ferrite Loaded Waveguides for LOM (HOM) damping with only 1 stub filter → simplified stub tuning, to fully decouple 1.4 GHz TM020 accelerating mode for 1st waveguide mode with cut off at:
Fc-TE11 = 867 MHz
Fc-TE21 = 1734 MHz (evanescent at 1.4 GHz)
Initial design: Vhhc_tot = 1.35 MV → Vhhc = 375 kV/cavity
NEW Requirement: Also overstretching operation:
Vhhc_tot = 1.65 MV → Vhhc = 413 kV/cav
In both cases - 3 HOM dampers for TMm2p modes and a few other HOM…
1 Ferrite Loaded Coaxial Line for LOM (HOM) damping with 3 stub filters to fully decouple 1.4 GHz TM020 accelerating mode for TEM & 3 TE higher modes with cut off at:
Fc-TE11 = 370 MHz
Fc-TE21 = 746 MHz
Fc-TE31 = 1100 MHz
Fc-TE41 = 1500 MHz (evanescent at 1.4 GHz)
(H-Fields)
 | R/Q [W] | Q | R [MW] | Vcav [kV] | Pcav [kW]
Initial design | 44 | 33500 | 1.47 | 375 | 48
New version | 45 | 40500 | 1.82 | 413 | 47
[Vincent Serrière]

## Slide 14: HarmonLip 2024
2nd HarmonLIP workshop
19th and 20th March, 2024 at the ESRF.
Workshop organized within the HarmonLIP (Leaps Internal Project)
Aims to foster information exchange and joint research efforts amongst the LEAPS members for the further development of harmonic cavity/bunch lengthening systems for present and future ultralow emittance storage rings.
Save the date !

## Slide 15: ESLS RF: An Exciting story of technical and scientific exchange
    My first ESLS RF meeting: 1998 at Elettra !
    Slides still hand made
    Harmonic RF already a subject
    Closing the loop today at Elettra !
    Power point since long
    Harmonic RF still or again an important subject
    I will retire coming July 2024:
    It’s my last ESLS RF today
    And it’s time to say:
    Farewell to all of you !
    Jörn

## Slide 16: Many thanks for your attention